## Slide 1: 虛擬化技術 Virtualization and Virtual Machines
Intel Virtualization Technology

## Slide 2: Agenda
CPU Virtualization: Intel VT-x
Memory Virtualization: Extended Page Tables (EPT)
IO Virtualization: Intel VT-d

## Slide 3: CPU Virtualization
Intel VT-x

## Slide 4: CPU Architecture
What is trap ?
  When CPU is running in user mode, some internal or external events, which need to be handled in kernel mode, take place.
  Then CPU will jump to hardware exception handler vector, and execute system operations in kernel mode.
Trap types :
  System Call
    Invoked by application in user mode.
    For example, application ask OS for system IO.
  Hardware Interrupts
    Invoked by some hardware events in any mode.
    For example, hardware clock timer trigger event.
  Exception
    Invoked when unexpected error or system malfunction occur.
    For example, execute privilege instructions in user mode.

## Slide 5: Trap and Emulate Model
If we want CPU virtualization to be efficient, how should we implement the VMM ?
  We should make guest binaries run on CPU as fast as possible.
  Theoretically speaking, if we can run all guest binaries natively, there will NO overhead at all.
  But we cannot let guest OS handle everything, VMM should be able to control all hardware resources.
Solution :
  Ring Compression
    Shift traditional OS from kernel mode(Ring 0) to user mode(Ring 1), and run VMM in kernel mode.
    Then VMM will be able to intercept all trapping event.

## Slide 6: Trap and Emulate Model
VMM virtualization paradigm (trap and emulate) :
  Let normal instructions of guest OS run directly on processor in user mode.
  When executing privileged instructions, hardware will make processor trap into the VMM.
  The VMM emulates the effect of the privileged instructions for the guest OS and return to guest.

## Slide 7: Trap and Emulate Model
Traditional OS :
  When application invoke a system call :
    CPU will trap to interrupt handler vector in OS.
    CPU will switch to kernel mode (Ring 0) and execute OS instructions.
  When hardware event :
    Hardware will interrupt CPU execution, and jump to interrupt handler in OS.

## Slide 8: Trap and Emulate Model
VMM and Guest OS :
  System Call
    CPU will trap to interrupt handler vector of VMM.
    VMM jump back into guest OS.
  Hardware Interrupt
    Hardware make CPU trap to interrupt handler of VMM.
    VMM jump to corresponding interrupt handler of guest OS.
  Privilege Instruction
    Running privilege instructions in guest OS will be trapped to VMM for instruction emulation.
    After emulation, VMM jump back to guest OS.

## Slide 9: Context Switch
Steps of VMM switch different virtual machines :
  Timer Interrupt in running VM.
  Context switch to VMM.
  VMM saves state of running VM.
  VMM determines next VM to execute.
  VMM sets timer interrupt.
  VMM restores state of next VM.
  VMM sets PC to timer interrupt handler of next VM.
  Next VM active.

## Slide 10: System State Management
Virtualizing system state :
  VMM will hold the system states of all virtual machines in memory.
  When VMM context switch from one virtual machine to another
    Write the register values back to memory
    Copy the register values of next guest OS to CPU registers.

## Slide 11: Virtualization Theorem
Subset theorem :
  For any conventional third-generation computer, a VMM may be constructed if the set of sensitive instructions for that computer is a subset of the set of privileged instructions.
Recursive Emulation :
  A conventional third-generation computer is recursively virtualizable if
    It is virtualizable
    VMM without any timing dependencies can be constructed for it.
Under this theorem, x86 architecture cannot be virtualized directly. Other techniques are needed.

## Slide 12: Virtualization Techniques
How to virtualize unvirtualizable hardware :
  Para-virtualization
    Modify guest OS to skip the critical instructions.
    Implement some hyper-calls to trap guest OS to VMM.
  Binary translation
    Use emulation technique to make hardware virtualizable.
    Skip the critical instructions by means of these translations.
  Hardware assistance
    Modify or enhance ISA of hardware to provide virtualizable architecture.
    Reduce the complexity of VMM implementation.

## Slide 13: Some Difficulties
Difficulties of binary translation :
  Self-modifying code
    If guest OS will modify its own binary code in runtime, binary translation need to flush the responding code cache and retranslate the code block.
  Self-reference code
    If guest code need to reference(read) its own binary code in runtime, VMM need to make it referring back to original guest binaries location.
  Real-time system
    For some timing critical guest OS, emulation environment will lose precise timing, and this problem cannot be perfectly solved yet.
Difficulty of para-virtualization :
  Guest OS modification
    User should at least has the source code of guest OS and modify its kernel; otherwise, para-virtualization cannot be used.

## Slide 14: Hardware Solution
Why are there so many problems and difficulties ?
  Critical instructions do not trap in user mode.
  Even if we make those critical instructions trap, their semantic may also be changed; which is not acceptable.
In short, legacy processors did not design for virtualization purpose at the beginning.
  If processor can be aware of the different behaviors between guest and host, the VMM design will be more efficient and simple.

## Slide 15: Hardware Solution
Let’s go back to trap model :
  Some trap types do not need the VMM involvement.
    For example, all system calls invoked by application in guest OS should be caught by gust OS only. There is no need to trap to VMM and then forward it back to guest OS, which will introduce context switch overhead.
  Some critical instructions should not be executed by guest OS.
    Although we make those critical instructions trap to VMM, VMM cannot identify whether this trapping action is caused by the emulation purpose or the real OS execution exception.
Solution :
  We need to redefine the semantic of some instructions.
  We need to introduce new CPU control paradigm.

## Slide 16: Intel VT-x
In order to straighten those problems out, Intel introduces one more operation mode of x86 architecture.
  VMX Root Operation (Root Mode)
    All instruction behaviors in this mode are no different to traditional ones.
    All legacy software can run in this mode correctly.
    VMM should run in this mode and control all system resources.
  VMX Non-Root Operation (Non-Root Mode)
    All sensitive instruction behaviors in this mode are redefined.
    The sensitive instructions will trap to Root Mode.
    Guest OS should run in this mode and be fully virtualized through typical “trap and emulation model”.

## Slide 17: Intel VT-x
VMM with VT-x :
  System Call
    CPU will directly trap to interrupt handler vector of guest OS.
  Hardware Interrupt
    Still, hardware events need to be handled by VMM first.
  Sensitive Instruction
    Instead of trap all privilege instructions, running guest OS in Non-root mode will trap sensitive instruction only.

## Slide 18: Pre & Post Intel VT-x
VMM de-privileges the guest OS into Ring 1, and takes up Ring 0
OS un-aware it is not running in traditional ring 0 privilege
Requires compute intensive SW translation to mitigate
VMM has its own privileged level
where it executes
No need to de-privilege the guest OS
OSes run directly on the hardware

## Slide 19: Context Switch
VMM switch different virtual machines with Intel VT-x :
  VMXON/VMXOFF
    These two instructions are used to turn on/off CPU Root Mode.
  VM Entry
    This is usually caused by the execution of VMLAUNCH/VMRESUME instructions, which will switch CPU mode from Root Mode to Non-Root Mode.
  VM Exit
    This may be caused by many reasons, such as hardware interrupts or sensitive instruction executions.
    Switch CPU mode from Non-Root Mode to Root Mode.

## Slide 20: System State Management
Intel introduces a more efficient hardware approach for register switching, VMCS (Virtual Machine Control Structure) :
  State Area
    Store host OS system state when VM-Entry.
    Store guest OS system state when VM-Exit.
  Control Area
    Control instruction behaviors in Non-Root Mode.
    Control VM-Entry and VM-Exit process.
  Exit Information
    Provide the VM-Exit reason and some hardware information.
Whenever VM Entry or VM Exit occur, CPU will automatically read or write corresponding information into VMCS.

## Slide 21: System State Management
Binding virtual machine to virtual CPU
  VCPU (Virtual CPU) contains two parts
    VMCS maintains virtual system states, which is approached by hardware.
    Non-VMCS maintains other non-essential system information, which is approach by software.
  VMM needs to handle Non-VMCS part.

## Slide 22: Memory Virtualization
Extended Page Tables (EPT)

## Slide 23: Hardware Solution
Difficulties of shadow page table technique :
  Shadow page table implementation is extremely complex.
  Page fault mechanism and synchronization issues are critical.
  Host memory space overhead is considerable.
But why we need this technique to virtualize MMU ?
  MMU do not first implemented for virtualization.
  MMU is knowing nothing about two level page address translation.
Now, let us consider hardware solution.

## Slide 24: Extended Page Table
Concept of Extended Page Table (EPT) :
  Instead of walking along with only one page table hierarchy, EPT technique implement one more page table hierarchy.
    One page table is maintained by guest OS, which is used to generate guest physical address.
    The other page table is maintained by VMM, which is used to map guest physical address to host physical address.
  For each memory access operation, EPT MMU will directly get guest physical address from guest page table, and then get host physical address by the VMM mapping table automatically.

## Slide 25: EPT Translation: Details
All guest-physical addresses go through extended page tables

## Slide 26: Memory Operation
8
9
6
4
7
8
Data

## Slide 27: IO Virtualization
Intel VT-d

## Slide 28: Hardware Solution
Difficulty :
  Software cannot make data access directly from devices.
Intel hardware solutions :
  Implement DMA remapping in hardware
    Remap DMA operations automatically by hardware.
    Intel VT-d

## Slide 29: Options For I/O Virtualization
Pro: Higher Performance
Pro: I/O Device Sharing
Pro: VM Migration
Con: Larger Hypervisor
Hypervisor
Shared Devices
I/O Services
Device Drivers
VM0
Guest OS
and Apps
VMn
Guest OS
and Apps
Monolithic Model
Pro: Highest Performance
Pro: Smaller Hypervisor
Pro: Device assisted sharing
Con: Migration Challenges
Assigned Devices
Hypervisor
VM0
Guest OS
and Apps
Device Drivers
VMn
Guest OS
and Apps
Device Drivers
Pass-through Model
VT-d Goal: Support all Models
Pro: High Security
Pro: I/O Device Sharing
Pro: VM Migration
Con: Lower Performance
Shared Devices
I/O Services
Hypervisor
Device Drivers
Service VMs
VMn
VM0
Guest OS
and Apps
Guest VMs
Service VM Model

## Slide 30: VT-d Overview
VT-d is platform infrastructure for I/O virtualization
  Defines architecture for DMA remapping
  Implemented as part of platform core logic
  Will be supported broadly in Intel server and client chipsets
VT-d
CPU
CPU
DRAM
South
Bridge
System Bus
PCI Express
PCI, LPC,
Legacy devices, …
Integrated
Devices
North Bridge
PCIe* Root Ports

## Slide 31: Intel VT-d
Add DMA remapping hardware component.
Software Approach
Hardware Approach

## Slide 32: Remapping Benefits
Protection:
  Enhance security and reliability through device isolation
  End to end isolation from VM to devices
Performance:
  Allows I/O devices to be directly assigned to specific virtual machines
  Eliminate Bounce buffer conditions with 32-bit devices
Efficiency:
  Interrupt isolation and load balancing
  System scalability with extended xAPIC support
Core platform infrastructure for Single Root IOV

## Slide 33: VT-d Architecture Detail
Memory-resident Partitioning And
Translation Structures
Device
Assignment
Structures
Address Translation
Structures
Device D1
Device D2
Address Translation
Structures
DMA Requests
Device ID
Virtual Address
Length
Memory Access with System Physical Address
DMA Remapping
Engine
Translation Cache
Context Cache
Fault Generation
…
Bus 255
Bus 0
Bus N
Page
Frame
4KB Page
Tables
Dev 31, Func 7
Dev P, Func 2
Dev 0, Func 0
Dev P, Func 1

## Slide 34: VT-d: Hardware Page Walk
000000b
Bus
Device
Func
0
2
3
7
8
15
Requestor ID
Device Assignment Tables
Base
Level-4
Page Table
Level-3
Page Table
Level-2
Page Table
Level-1
Page Table
Page
Example Device Assignment Table Entry specifying 4-level page table
56
DMA Virtual Address
0
11
Level-4
table offset
Level-3 table offset
Level-2 table offset
Level-1 table offset
12
20
21
29
30
38
39
47
000000000b
63
48
57
Page Offset

## Slide 35: VT-d: Translation Caching
Architecture supports caching of remapping structures
  Context Cache: Caches frequently used device-assignment entries
  IOTLB: Caches frequently used translations (results of page walk)
  Non-leaf Cache: Caches frequently used page-directory entries
When updating VT-d translation structures, software enforces consistency of these caches
  Architecture supports global, domain-selective, and page-range invalidations of these caches
  Primary invalidation interface through MMIO registers for synchronous invalidations
  Extended invalidation interface for queued invalidations

## Slide 36: VT-x & VT-d Working Together
Binary Translation
Paravirtualization
Page-table Shadowing
IO-Device Emulation
Interrupt Virtualization
DMA Remap
Physical Memory
I/O Devices
Logical Processors
Virtual Machine Monitor (VMM)
Virtual Machines
Hardware Virtualization Mechanisms under VMM Control
VT-x
VT-d

## Slide 37: Summary
CPU Virtualization
  Trap and Emulate Model
  Virtualization technique, VMX Root/Non-Root Operation, VMM and Guest OS, VMCS … etc.
Memory Virtualization: Extended Page Tables (EPT)
  EPT implement one more page table hierarchy
  MMU virtualize, EPT translation, Memory Operation,… etc.
IO Virtualization: Intel VT-d
  Implement DMA remapping in hardware
  Hardware Page Walk, Translation Caching

## Slide 38: References
Paper:
  Uhlig, Rich, et al. "Intel virtualization technology." Computer 38.5 (2005): 48-56.
Web resources:
  Intel Virtualization Technology: Strategy and Evolution - Microsoft http://download.microsoft.com/download/5/b/9/5b97017b-e28a-4bae-ba48-174cf47d23cd/vir054_wh06.ppt
  Intel® Virtualization Transforms IT http://www.intel.com/content/www/us/en/virtualization/intel-virtualization-transforms-it.html