## Slide 1: 虛擬化技術 Virtualization Techniques
Network Virtualization
InfiniBand Virtualization

## Slide 2: Agenda
Overview
  What is InfiniBand
  InfiniBand Architecture
InfiniBand Virtualization
  Why do we need to virtualize InfiniBand
  InfiniBand Virtualization Methods
  Case study

## Slide 3: Agenda
Overview
  What is InfiniBand
  InfiniBand Architecture
InfiniBand Virtualization
  Why do we need to virtualize InfiniBand
  InfiniBand Virtualization Methods
  Case study

## Slide 4: IBA
The InfiniBand Architecture (IBA) is a new industry-standard architecture for server I/O and inter-server communication.
  Developed by InfiniBand Trade Association (IBTA).
It defines a switch-based, point-to-point interconnection network that enables
  High-speed
  Low-latency
  communication between connected devices.

## Slide 5: InfiniBand Devices
Adapter Card
Cable
Switch

## Slide 6: Usage
InfiniBand is commonly used in high performance computing (HPC).
InfiniBand 44.80%
Gigabit Ethernet
37.80%

## Slide 7: InfiniBand VS. Ethernet
 | Ethernet | InfiniBand
Commonly used in what kinds of network | Local area network(LAN) or wide area network(WAN) | Interprocess communication (IPC) network
Transmission medium | Copper/optical | Copper/optical
Bandwidth | 1Gb/10Gb | 2.5Gb~120Gb
Latency | High | Low
Popularity | High | Low
Cost | Low | High

## Slide 8: Agenda
Overview
  What is InfiniBand
  InfiniBand Architecture
InfiniBand Virtualization
  Why do we need to virtualize InfiniBand
  InfiniBand Virtualization Methods
  Case study

## Slide 9: InfiniBand Architecture
The IBA Subnet
Communication Service
Communication Model
Subnet Management

## Slide 10: IBA Subnet Overview
IBA subnet is the smallest complete IBA unit.
  Usually used for system area network.
Element of a subnet
  Endnodes
  Links
  Channel Adapters(CAs)
    Connect endnodes to links
  Switches
  Subnet manager

## Slide 11: IBA Subnet

## Slide 12: Endnodes
IBA endnodes are the ultimate sources and sinks of communication in IBA.
  They may be host systems or devices.
    Ex. network adapters, storage subsystems, etc.

## Slide 13: Links
IBA links are bidirectional point-to-point communication channels, and may be either copper and optical fibre.
  The base signalling rate on all links is 2.5 Gbaud.
    Link widths are 1X, 4X, and 12X.

## Slide 14: Channel Adapter
Channel Adapter (CA) is the interface between an endnode and a link
There are two types of channel adapters
  Host channel adapter(HCA)
    For inter-server communication
    Has a collection of features that are defined to be available to host programs, defined by verbs
  Target channel adapter(TCA)
    For server IO communication
    No defined software interface

## Slide 15: Switches
IBA switches route messages from their source to their destination based on routing tables
  Support multicast and multiple virtual lanes
Switch size denotes the number of ports
  The maximum switch size supported is one with 256 ports
The addressing used by switched
  Local Identifiers, or LIDs allows 48K endnodes on a single subnet
  The 64K LID address space is reserved for multicast addresses
  Routing between different subnets is done on the basis of a Global Identifier (GID) that is 128 bits long

## Slide 16: Addressing
LIDs
  Local Identifiers, 16 bits
  Used within a subnet by switch for routing
GUIDs
  Global Unique Identifier
  64 EUI-64 IEEE-defined identifiers for elements in a subnet
GIDs
  Global IDs, 128 bits
  Used for routing across subnets

## Slide 17: InfiniBand Architecture
The IBA Subnet
Communication Service
Communication Model
Subnet Management

## Slide 18: Communication Service Types

## Slide 19: Data Rate
Effective theoretical throughput

## Slide 20: InfiniBand Architecture
The IBA Subnet
Communication Service
Communication Model
Subnet Management

## Slide 21: Queue-Based Model
Channel adapters communicate using Work Queues of three types:
  Queue Pair(QP) consists of
    Send queue
    Receive queue
  Work Queue Request (WQR) contains the communication instruction
    It would be submitted to QP.
  Completion Queues (CQs) use Completion Queue Entries (CQEs) to report the completion of the communication

## Slide 22: Queue-Based Mode

## Slide 23: Access Model for InfiniBand
Privileged Access
  OS involved
  Resource management and memory management
    Open HCA, create queue-pairs, register memory, etc.
Direct Access
  Can be done directly in user space (OS-bypass)
  Queue-pair access
    Post send/receive/RDMA descriptors.
  CQ polling

## Slide 24: Access Model for InfiniBand
Queue pair access has two phases
  Initialization (privileged access)
    Map doorbell page (User Access Region)
    Allocate and register QP buffers
    Create QP
  Communication (direct access)
    Put WQR in QP buffer.
    Write to doorbell page.
      Notify channel adapter to work

## Slide 25: Access Model for InfiniBand
CQ Polling has two phases
  Initialization (privileged access)
    Allocate and register CQ buffer
    Create CQ
  Communication steps (direct access)
    Poll on CQ buffer for new completion entry

## Slide 26: Memory Model
Control of memory access by and through an HCA is provided by three objects
  Memory regions
    Provide the basic mapping required to operate with virtual address
    Have R_key for remote HCA to access system memory and L_key for local HCA to access local memory.
  Memory windows
    Specify a contiguous virtual memory segment with byte granularity
  Protection domains
    Attach QPs to memory regions and windows

## Slide 27: Communication Semantics
Two types of communication semantics
  Channel semantics
    With traditional send/receive operations.
  Memory semantics
    With RDMA operations.

## Slide 28: Send and Receive
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Remote Process
Process
Fabric
WQE

## Slide 29: Send and Receive
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Remote Process
Process
WQE
Fabric
WQE

## Slide 30: Send and Receive
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
WQE
Remote Process
Process
Fabric
WQE
Data packet

## Slide 31: Send and Receive
Remote Process
Process
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Complete
CQE
CQE
Fabric

## Slide 32: RDMA Read / Write
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Remote Process
Process
Fabric
Target Buffer

## Slide 33: RDMA Read / Write
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Remote Process
Process
WQE
Fabric
Target Buffer

## Slide 34: RDMA Read / Write
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
WQE
Remote Process
Process
Fabric
Data packet
Target Buffer
Read / Write

## Slide 35: RDMA Read / Write
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Transport Engine
Channel
Adapter
QP
Send Recv
CQ
Port
Remote Process
Process
Complete
CQE
Fabric
Target Buffer

## Slide 36: InfiniBand Architecture
The IBA Subnet
Communication Service
Communication Model
Subnet Management

## Slide 37: Two Roles
Subnet Managers(SM) : Active entities
  In an IBA subnet, there must be a single master SM.
  Responsible for discovering and initializing the network, assigning LIDs to all elements, deciding path MTUs, and loading the switch routing tables.
Subnet Management Agents :Passive entities.
  Exist on all nodes.
IBA Subnet
Master Subnet Manager
Subnet Management Agents
Subnet Management Agents
Subnet Management Agents
Subnet Management Agents

## Slide 38: Initialization State Machine

## Slide 39: Management Datagrams
All management is performed in-band, using Management Datagrams (MADs).
  MADs are unreliable datagrams with 256 bytes of data (minimum MTU).
Subnet Management Packets (SMP) is special MADs for subnet management.
  Only packets allowed on virtual lane 15 (VL15).
  Always sent and receive on Queue Pair 0 of each port

## Slide 40: Agenda
Overview
  What is InfiniBand
  InfiniBand Architecture
InfiniBand Virtualization
  Why do we need to virtualize InfiniBand
  InfiniBand Virtualization Methods
  Case study

## Slide 41: Cloud Computing View
Virtualization is usually used in cloud computing
  It would cause overhead and lead to performance degradation

## Slide 42: Cloud Computing View
The performance degradation is especially large for IO virtualization.
Chart: 
| physical machine | virtual machine
 | 24.834 | 0.345
PTRANS (Communication utilization)
GB/s
PM
KVM

## Slide 43: High Performance Computing View
InfiniBand is widely used in the high-performance computing center
  Transfer supercomputing centers to data centers
  For HPC on cloud
    Both of them would need to virtualize the systems
    Consider the performance and the availability of the existed InfiniBand devices, it would need to virtualize InfiniBand

## Slide 44: Agenda
Overview
  What is InfiniBand
  InfiniBand Architecture
InfiniBand Virtualization
  Why do we need to virtualize InfiniBand
  InfiniBand Virtualization Methods
  Case study

## Slide 45: Three kinds of methods
Fully virtualization: software-based I/O virtualization
  Flexibility and ease of migration
    May suffer from low I/O bandwidth and high I/O latency
Bypass: hardware-based I/O virtualization
  Efficient but lacking of flexibility for migration
Paravirtualization: a hybrid of software-based and hardware-based virtualization.
  Try to balance the flexibility and efficiency of virtual I/O.
  Ex. Xsigo Systems.

## Slide 46: Fully virtualization

## Slide 47: Bypass

## Slide 48: Paravirtualization
Software Defined Network
/InfiniBand

## Slide 49: Agenda
Overview
  What is InfiniBand
  InfiniBand Architecture
InfiniBand Virtualization
  Why do we need to virtualize InfiniBand
  InfiniBand Virtualization Methods
  Case study

## Slide 50: Agenda
What is InfiniBand
  Overview
  InfiniBand Architecture
Why InfiniBand Virtualization
InfiniBand Virtualization Methods
  Methods
  Case study

## Slide 51: VMM-Bypass I/O Overview
Extend the idea of OS-bypass originated from user-level communication
Allows time critical I/O operations to be carried out directly in guest virtual machines without involving virtual machine monitor and a privileged virtual machine

## Slide 52: InfiniBand Driver Stack
OpenIB Gen2 Driver Stack
  HCA Driver is hardware dependent

## Slide 53: Design Architecture

## Slide 54: Implementation
Follows Xen split driver model
  Front-end implemented as a new HCA driver module (reusing core module) and it would create two channels
    Device channel for processing requests initiated from the guest domain.
    Event channel for sending InifiniBand CQ and QP events to the guest domain.
  Backend uses kernel threads to process requests from front-ends (reusing IB drivers in dom0).

## Slide 55: Implementation
Privileged Access
  Memory registration
  CQ and QP creation
  Other operations
VMM-bypass Access
  Communication phase
Event handling

## Slide 56: Privileged Access
Memory registration
Back-end
driver
Front-end
driver
Memory pinning
Translation
1
Send physical page information
2
Native HCA driver
Register
physical page
3
HCA
Send local and remote key
4

## Slide 57: Privileged Access
Guest Domain
  CQ and QP creation
Back-end
driver
Front-end
driver
Allocate CQ and QP buffer
1
Register CQ and QP buffers
2
Send requests with CQ, QP buffer keys
3
Create CQ, QP using those keys
4

## Slide 58: Privileged Access
Other operations
Back-end
driver
Front-end
driver
Native HCA driver
Send requests
1
Process requests
2
Send back results
3
IB operation
Resource Pool
(Including QP, CQ, and etc.)
Each resource has itself handle number which as a key to get resource.
Keep:
Keep:

## Slide 59: VMM-bypass Access
Communication phase
  QP access
    Before communication, doorbell page is mapped into address space (needs some support from Xen).
    Put WQR in QP buffer.
    Ring the doorbell.
CQ polling
  Can be done directly.
    Because CQ buffer is allocated in guest domain.

## Slide 60: Event Handling
Event handling
  Each domain has a set of end-points(or ports) which may be bounded to an event source.
  When a pair of end-points in two domains are bound together, a “send” operation on one side will cause
    An event to be received by the destination domain
    In turn, cause an interrupt.

## Slide 61: Event Handling
CQ, QP Event handling
  Uses a dedicated device channel (Xen event channel + shared memory)
  Special event handler registered at back-end for CQs/QPs in guest domains
    Forwards events to front-end
    Raise a virtual interrupt
  Guest domain event handler called through interrupt handler

## Slide 62: Case study
VMM-Bypass I/O
Single Root I/O Virtualization

## Slide 63: SR-IOV Overview
SR-IOV (Single Root I/O Virtualization) is a specification that is able to allow a PCI Express device appears to be multiple physical PCI Express devices.
  Allows an I/O device to be shared by multiple Virtual Machines(VMs).
SR-IOV needs support from BIOS and operating system or hypervisor.

## Slide 64: SR-IOV Overview
There are two kinds of functions:
  Physical functions (PFs)
    Have full configuration resources such as discovery, management and manipulation
  Virtual functions (VFs)
    Viewed as “light weighted” PCIe function.
    Have only the ability to move data in and out of devices.
SR-IOV specification shows that each device can have up to 256 VFs.

## Slide 65: Virtualization Model
Hardware controlled by privileged software through PF.
VF contain minimum replicated resources
  Minimum configure space
  MMIO for direct communication.
  RID for DMA traffic index.

## Slide 66: Implementation
Virtual switch
  Transfer the received data to the right VF
Shared port
  The port on the HCA is shared between PFs and VFs.

## Slide 67: Implementation
Virtual Switch
  Each VF acts as a complete HCA.
    Has unique port (LID, GID Table, and etc).
    Owns management QP0 and QP1.
  Network sees the VFs behind the virtual switch as the multiple HCA.
Shared port
  Single port shared by all VFs.
    Each VF uses unique GID.
  Network sees a single HCA.

## Slide 68: Implementation
Shared port
  Multiple unicast GIDs
    Generated by PF driver before port is initialized.
    Discovered by SM.
      Each VF sees only a unique subset assigned to it.
  Pkeys, index for operation domain partition, managed by PF
    Controls which Pkeys are visible to which VF.
    Enforced during QP transitions.

## Slide 69: Implementation
Shared port
  QP0 owned by PF
    VFs have a QP0, but it is a “black hole”.
      Implies that only PF can run SM.
  QP1 managed by PF
    VFs have a QP1, but all Management Datagram traffic is tunneled through the PF.
  Shared Queue Pair Number(QPN) space
    Traffic multiplexed by QPN as usual.

## Slide 70: Mellanox Driver Stack

## Slide 71: ConnectX2 Support Function
Functions contain ─
  Multiple PFs and VFs.
  Practically unlimited hardware resources.
    QPs, CQs, SRQs, Memory regions, Protection domains
    Dynamically assigned to VFs upon request.
  Hardware communication channel
    For every VF, the PF can
      Exchange control information
      DMA to/from guest address space
    Hypervisor independent
      Same code for Linux/KVM/Xen

## Slide 72: ConnectX2 Driver Architecture
mlx4_core module
PF
Device ID
mlx4_core module
VF
Device ID
Have
UARs
Protection Domain
Element Queue
  MSI-X vectors
ConnextX2 Device
Hands off Firmware Command and resource allocation of VM
Allocates resources
Accepts VF command and executes
Main Work：
Para-virtualize shared resources
Same Interface driver─
mlx4_ib
mlx4_en
mlx4_fc

## Slide 73: ConnectX2 Driver Architecture
PF/VF partitioning at mlx4_core module
  Same driver for PF/VF, but with different works.
  Core driver is identified by Device ID.
VF work
  Have its User Access Regions, Protection Domain, Element Queue, and MSI-X vectors
  Handle firmware commands and resource allocation to PF
PF work
  Allocates resources
  Executes VF commands in a secure way
  Para-virtualizes shared resources
Interface drivers (mlx4_ib/en/fc) unchanged
  Implies IB, RoCEE, vHBA (FCoIB / FCoE) and vNIC (EoIB)

## Slide 74: Xen SRIOV SW Stack
IOMMU
Hypervisor
ConnectX
mlx4_core
mlx4_core
mlx4_ib
mlx4_en
mlx4_fc
DomU
Dom0
ib_core
scsi
mid-layer
Communication
channel
Interrupts and dma from/to device
Doorbells
HW commands
tcp/ip
guest-physical to machine
address translation
mlx4_ib
mlx4_en
mlx4_fc
ib_core
scsi
mid-layer
tcp/ip
Interrupts and dma from/to device
Doorbells
1
2
3
3
4
4

## Slide 75: KVM SRIOV SW Stack
IOMMU
ConnectX
Guest Process
Kernel
Communication
channel
Interrupts and dma from/to device
Doorbells
HW commands
mlx4_core
mlx4_ib
mlx4_en
mlx4_fc
ib_core
scsi mid-layer
tcp/ip
guest-physical to machine
address translation
Interrupts and dma from/to device
Doorbells
mlx4_core
mlx4_ib
mlx4_en
mlx4_fc
ib_core
scsi mid-layer
tcp/ip
User
User
Kernel
Linux
1
2
3
3
4
4

## Slide 76: References
An Introduction to the InﬁniBand™ Architecture
  http://gridbus.csse.unimelb.edu.au/~raj/superstorage/chap42.pdf
J. Liu, W. H., B. Abali and D. K. Panda, "High Performance VMM-Bypass I/O in Virtual Machines", in USENIX Annual Technical Conferencepp, 29-42 (June 2006)
Infiniband and RoCEE Virtualization with SR-IOV
  http://www.slideshare.net/Cameroon45/infiniband-and-rocee-virtualization-with-sriov